## Slide 1: Electrolysis
Mr Dhue
(with slight modification)

## Slide 2
Outline
From your syllabus:
Science Understanding
electrolytic cells use an external electrical potential difference to provide the energy to allow a non-spontaneous redox reaction to occur
describe the use of electrolysis in electrolytic refining, including for purification of copper, and metal electroplating, including for silver

## Slide 3
In a voltaic cell, a spontaneous chemical reaction takes place in which stored chemical energy is converted into electrical energy.
The cell develops an EMF which depends on the particular oxidation and reduction reactions at the electrodes and the concentration of the electrolyte solution.
Introduction

## Slide 4: Remember the Daniell Cell ?

## Slide 5: What would happen to place a battery in the external circuit in opposite polarity to that of the cell ?

## Slide 6
If the applied voltage is at least 1.10 V the electrode reactions are reversed and zinc and copper (II) ions will be formed by the cell.
Note the half cells have swapped from anode to cathode (and vis versa) as the oxidation and reduction processes have swapped.
This reaction is not spontaneous and converts electrical energy for the reaction to proceed.
This process is called electrolysis
An electrochemical cell that electrolysis occurs is called an electrolytic cell.

## Slide 7
Comparison: galvanic vs electrolytic

## Slide 8
The identification of anode (oxidation) and cathode (reduction) is the same for both galvanic and electrolytic cells.
The polarity for the anode and cathode is different for galvanic and electrolytic cells

## Slide 9: Two types of electrochemical cells
Voltaic Cell (or Galvanic Cell) | Electrolytic Cell
A spontaneous reaction to generate electrical energy | Uses electrical energy to drive a non-spontaneous reaction
EP reactants > EP products | Electrical energy converts lower EP reactants to higher energy products
Can do work on the surroundings. | Work is done on the reacting system
Eg Batteries | Eg metal plating
Voltaic Cell | Electrolytic Cell
Anode (-ve) Cathode (+ve) | Anode (+ve) Cathode (-ve)

## Slide 10: Electrolytic cells can have both electrodes immersed in the same electrolyte

## Slide 11
Electrolysis of molten salts
Uses a pair of inert electrodes (e.g platinum electrodes)
The electrodes are dipped into the molten salt and are connected to a DC electric power supply

## Slide 12
Electrolysis of molten salts
Summary
The product at each electrode is simple if the molten salt is pure.
The electrolyte is the molten salt itself.
The cation will be reduced and the anion will be oxidised.
This is used industrially to produce active metals such as Na, Ca and Mg as well as halogens Cl2 and Br2

## Slide 13
Electrolysis of an aqueous solution
It is more difficult to predict the outcome for electrolysis in aqueous solutions as the water may be oxidised and reduced preferentially
Likewise, if you use reactive electrodes they might preferentially react

## Slide 14
Electrolysis of an aqueous solution
Pure water is difficult to electrolyse because there are very few ions present to carry a current [H+] = [OH-] = 10-7 molL-1
If a small amount of a non-reacting salt is added (or a few drops of conc H2SO4) the process occurs rapidly.

## Slide 15
Electrolysis of an aqueous solution
Changes in these cells can be inferred from the observations:
  If water is oxidised then a colourless gas is formed at the anode and the solution pH falls in the vicinity of the anode.
  Anode reaction: 2H2O(l)  O2(g) + 4H+(aq) + 4e-
  If water is reduced then a colourless gas is formed at the cathode and the pH rises near the cathode.
  Cathode reaction: 2H2O(l) + 2e-  H2(g) + 2OH-(aq)
  If metallic electrode is oxidised than the anode will dissolve (reduce is size)

## Slide 16
Electrolysis of an aqueous solution
*Predictions using the SRP table are limited as most electrolytic cells are not at standard conditions*

## Slide 17: Types of electrolysis reactions
Electrolytic cells are often used to decompose compounds into elements and have important industrial importance. Eg Al, Cl2, Cu, Na
Can be used to purify elements as well as metal plate items. Eg Au refining, Cr plating.
Predicting products depends on nature of electrolysis reaction, such as molten or aqueous.

## Slide 18: The Lead acid accumulator (aka car battery)

## Slide 19: Electrorefining
Notes: Get high purity easy to achieve, more reactive metals are oxidised but stay in the solution. Also used for gold.

## Slide 20: Electrorefining
Keeping the voltage low allows for the separation of copper from various metal impurities

## Slide 21: Electroplating
Notes: Improve appearance Ag plating spoons etc, reduce corrosion eg Cr plating junk jewelrey

## Slide 22: Electroplating

## Slide 23: Electroplating