## Slide 4: What causes car crashes?
Write down everything you can think of

## Slide 5: Break it down:
Human factors
Car or road factors

## Slide 7: Thinking distance
What effects the thinking distance?
x

## Slide 8
Brakes have been applied
Braking distance
What effects the braking distance?

## Slide 9: Thinking distance
Braking distance
Stopping distance

## Slide 10: Stopping a car…
Braking distance
Too much alcohol
Thinking distance
Tiredness
Too many drugs
Wet roads
Driving too fast
Tyres/brakes worn out
Icy roads
Poor visibility
+

## Slide 11: Experiment
Get your partner to drop the ruler vertically.
React and catch it!

## Slide 12: Reaction times. What is your reaction time?
 | Reaction time
10cm 20cm 30cm 40cm 50cm | 0.14s 0.20s 0.24s 0.28s 0.31s
Task: Measure it three times and take an average.

## Slide 13: Reaction time ___ secs
Speed (mph) | Speed (m/s) | Thinking distance (speed x reaction time)
20 | 8.9 | 
30 | 13.4 | 
40 | 17.8 | 
50 | 22.3 | 
60 | 26.8 | 
70 | 31.2 | 
80 | 35.7 | 
100 | 44.7 | 

## Slide 14: Guess… What is the stopping distance of a car travelling at 70mph? (National speed limit on a motorway)

## Slide 16: So… why are these the same distance apart in all three lanes?...

## Slide 17: H/w Make a poster outlining the factors that effect cars stopping
Include statistics on distances for different speeds/roads
Break it into two:
Thinking distance (driver’s reaction distance)
Braking distance (distance it takes the car to stop after the driver has applied the brakes)